## Slide 1
Robot’s Concept This season, we focused on the concept of “a strong robot that moves accurately” and made improvements to the sensors, structural design, and drive performance. For visual sensors, we combined an Open MV camera with an omni-directional mirror to enable the robot to recognize the entire court with only one camera. For ball detection, a system consists of 16 balls sensors placed in a circle, is used to provide more accurate angle detection. In particular, the ball sensor system eliminates the pin count limitation of microcontrollers by using a multiplexer. Significant enhancements have also been made to offensive performance. A newly designed kicker device and a capture zone that fits the shape of the ball, made by a 3D printer, reduces the number of kick failure. This dramatically improves the stability and power of the shot, and enables stable forward delivery of the ball. As a result, we managed to improve its performance as a "robot that can surely score goals”. The DIGILENT IG22 1/19 motor is used for the drive system to achieve a good balance of controllability and power of the robot. Furthermore, the two-layer omni wheel, which has evolved from a single-layer structure, provides both high traction and smooth movement. We also focused on making it easy to repair and debug the robot during the game. The on-board OLED Display enables us to check the real-time sensor data for quick troubleshooting and adjustments, eliminating the need for a PC connection and greatly improving the maintenance performance. As a main microcontroller, we chosen Teensy 4.0, ensuring high-speed communication and rich I/O expandability. In addition, we have placed emphasis on maintainability and stability through the use of flat cables, LEDs, and wiring design that takes noise suppression into consideration. Also, we used to manufacture the attacker and goalkeeper robot separately. But from this time, both robots share all sensors and circuit boards, simplifying parts management and achieving a high degree of interchangeability.
I2C
Method / Production / Design
Munako Aegis
Soccer LWL
League
JAPAN
Munakata High School
Team Name
Our School
Region
Abstract
Maiki Kimura
Umi Fujita
Yuta Kurisaki
Koki Suehiro
Team Member
Aircraft and Circuit Design Manager
Goalkeeper Program Manager
Software
Hardware
Attacker Program Manager
Team X
Team GitHub
Sponsor
Circuit Design, Media Manager
Team Activities
Smoothing Sensor Readings Using Moving Average
There were some fluctuations in the analog values from the ball sensor. To reduce this, we applied
a moving average filter to the sensor readings. We rolled the ball away from the sensor and observed the changes in the readings. We analyzed how the variation changed with different numbers of moving average samples and finally chose 10 samples. The graph below compares the results with and without the moving average.
Result：
The graph shows that applying a moving average filter makes the sensor readings smoother. Based on this result, we also applied the moving average to the analog values of the line sensor,
not just the ball sensor.
・KiCad
Used for circuit fabrication
Our team mainly uses the following software.
・ GitHub
Used for data storage
・ Visual Studio
Used for programming (except for the camera) with C++
Design
・Autodesk Fusion
Used for designing
the robot’s frame and components
Program
・ OpenMV IDE
Used for programming the camera with Python
・ Discord
Used for sharing information among team members
Management
Tool
Chart: robot effort
| 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261 | 45292 | 45323 | 45352 | 45383 | 45413 | 45444 | 45474 | 45505 | 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717 | 45748 | 45778 | 45809
robot effort | 7560 | 14520 | 21900 | 29460 | 36420 | 43980 | 50940 | 58500 | 65460 | 72420 | 79980 | 86940 | 94500 | 101460 | 108840 | 116400 | 123360 | 130920 | 137880 | 145440 | 152400 | 159360 | 166920 | 173880 | 181440 | 188400
１年目（前半）
１年目（後半）
2年目（前半）
2年目（後半）
世界大会へ
01 Vision System
The OpenMV H7 is limited to a viewing angle of about 70 degrees when used as a stand-alone camera, which is not enough for the robot to simultaneously grasp all directions of its surroundings. Therefore, we combined the OpenMV H7 with an Omnidirectional Mirror to create a system that allows the robot to acquire 360-degree omnidirectional images. The Omnidirectional Mirror is made of polyvinyl chloride (PVC), which is softened by heating and then pressed (heat-pressed) onto a hyperboloid surface made with a 3D printer to match the ideal shape designed on a computer. This can then be used to reflect it back to the camera, making it possible to acquire information from all directions with a single camera.
11.1V
02 Debug System
Debug System By equipping the robot with an O-LED display, it is now possible to view data from the sensor in real time. This allows for quick assessment of the robot's status and the surrounding situation on the spot, enabling more rapid and flexible tactical changes and troubleshooting. Previously, to check sensor data, the robot had to be stopped, connected to a computer, and the data reviewed. However, the introduction of the OLED Display has significantly reduced this effort. Especially in situations where quick on-site decision-making and response speed are required within limited match time, this provides a significant advantage. Additionally, it is also utilized for on-site debugging, contributing to improved development efficiency.
Omnidirectional Mirror
03 IR Board
Until now, we have only been able to mount up to eight ball (infrared) sensors on the Seeduino XIAO due to pin count limitations. This configuration enabled angle detection, but the wide spacing between sensors resulted in low detection accuracy and error. We introduced a multiplexer to solve this problem. This technical innovation made it possible to deploy 16 ball sensors The increase in the number of sensors has narrowed the distance between each sensor, allowing angles to be detected with higher accuracy.
before
after
08 Ball Capture Zone & solenoid
We have one new kicker (CB1037) on our robot this season. In order to maximize the performance of this kicker device , we devised a way to fully convey the power of the kicker device to the ball. Of particular importance was to ensure that the ball was well caught when kicked. Previously, even if the ball was caught, it did not mesh well with the kicker s device mechanism and could not be shot. To solve this problem, we utilized a 3D printer to create a “ball-capture zone” that fits the shape of the ball perfectly. This enabled the ball to be reliably captured. This design change was aimed at greatly increasing the success rate of the kick, solving the previous capture force problem and significantly improving the accuracy of the robot. By optimizing the shape of the ball-capturing zone, the force of the kick was transmitted more firmly to the ball, enabling the ball to fly at a more accurate angle, giving the robot an advantage in close matches against its opponents at national tournaments.
06 Motor & Omni Wheel
This season's robot features several improvements in the drive system. First, the robot is equipped with four DIGILENT IG22 1/19 high-precision gear motors, which provide higher torque and more stable power performance than . These motors are controlled by a 4CH motor controller (DSR1202). The structure of the omni wheel has also been improved to enhance the stability and controllability of the robot. By changing from a conventional one-layer structure to a two-layer structure, the grip has been improved, enabling the robot to maintain stable traveling performance even in situations where complex movements and fine control are required. In addition, our omni wheel has a larger diameter than the previous one, which allowed us to increase its speed. The inner part of the omni wheel is made of 3D printed parts, and the outer part is made of duralumin. This made it easier to mass produce and less prone to breakage.
07 Line Sensor
This season's robot is equipped with a more advanced line detection system that combines a circular line sensor with front, rear, and side line sensors. First, the line sensor is equipped with more LEDs than last time. This makes it possible to accurately detect white lines over a wide area in front, behind, and to the sides of the robot. The sensors use Seeduino XIAO for data reading, but due to port limitations, there was initially a limit to the number of sensors that could be installed. By introducing a multiplexer, we successfully increased the number of sensors that could be installed. This sensor system is particularly effective in goalkeeper robots. It enables accurate tracking of white lines, ensuring stable operation throughout play. The circular line sensor plays an important role in determining the direction of travel. By accurately detecting this, the robot can maintain the correct trajectory at all times. Furthermore, the robot used in the national competition frequently going out of bounds. By revising the configuration of the line sensors, we successfully reduced the “non-responsive blind spots” that existed under the robot. This further improved the overall line detection accuracy and significantly reduced the number of going out of bounds. Furthermore, by switching from the previously used light-modulated photodiode IC to a phototransistor this season, we have achieved significant cost savings while maintaining performance.
04 Main Board
The main board uses Teensy 4.0 and has 7 UARTs, 40 digital pins, 14 analog pins, and abundant pin counts. The main board design uses flat cables to reduce the number of cables. In addition, curves are used in the wiring design to reduce the effects of noise, which enhances the stability of the signal and the overall operational reliability of the robot. An LED is provided on the board to visually check the energized state, preventing human error. By clearly indicating the connection points, not only prevents wiring errors, but also contributes to more efficient programming work. Our robots are designed to be equipped with two types of gyro-sensors. This is so that if one sensor fails, we can instantly switch to the other by replacing the program. This backup design ensures that stable operation is maintained even if a sensor malfunctions during competition.
05 Power Board & Kicker Board
Previously, the power board and kicker board were manufactured separately, but from this season they have been integrated to save space and simplify wiring. This has made the robot's internal structure more compact and greatly improved the efficiency of assembly and parts replacement. The power supply board uses a DC DC converter and is designed to provide stable power to each module. This minimizes voltage fluctuations during operation and improves overall system stability. The kicker circuit also incorporates a voltage booster circuit, which is designed to provide a stable output of high voltage (48V).
09 Frame
The frame that forms the base of the robot is made of duralumin (aluminum alloy). Duralumin is a metal material that is so strong that it is used in aircraft, and is also extremely lightweight. By taking advantage of these characteristics, we were able to achieve a design that combines durability and lightness. In addition, we have achieved a structure that reduces weight while maintaining strength by performing hollow processing on unnecessary parts while maintaining the necessary strength of the frame. The frame design was created using Fusion 360, and the actual machining is performed on the CNC milling machine available within the club.
We are “Munako Aegis,” a team of four Japanese high school students competing in the Lightweight League.
We began our activities in the 2023 season and have been steadily improving our skills through daily, dedicated work on our robot.
When we first started, none of us had any specialized skills. However, we tackled mechanical design, programming, and circuit design every day, gaining knowledge and experience through trial and error.
In our first year, we placed first in the preliminary competition and qualified for the Japan Open. However, we finished a disappointing 31st out of 64 teams in the main event.
Nevertheless, we didn't give up and kept working hard. This year, we won first place at the Japan Open. We also won the Best Presentation Award.
We primarily use Autodesk Fusion for mechanical design and KiCad for circuit design. For fabrication, we utilize 3D printers and CNC milling machines to develop robots efficiently and with high precision.
We write programs in Visual Studio Code, using C++ for the microcontroller and Micro Python for camera control, developed with the Open MV IDE.
Our robot uses duralumin for its body to combine light weight with high durability. We made exterior components, such as the battery box and side covers, ourselves using a 3D printer, allowing for design flexibility. For the circuit board, we asked our sponsor, JLCPCB, to fabricate it with high precision to achieve a stable circuit configuration.
The camera system uses an Omnidirectional Mirror, which we made ourselves by heat-pressing vinyl chloride. This allows a single camera to provide a 360-degree field of view while significantly reducing costs.
In addition, a kicker mechanism is installed using a solenoid provided by TAKAHA.
To address the “line-out” issue that many teams have struggled with in recent years, we incorporated speed control.
The robot measures its speed in real time as it moves and runs at the optimum speed according to its court position to prevent line-outs at the fastest possible speed.
In addition, we use a double-structured omni wheel design. The double structure increases the ground contact area with the floor and improves braking ability.
Red LEDs are used for the line sensor to improve response speed and accuracy. These innovations strengthen the line area.
For ball detection, we use a multiplexer to handle multiple inputs despite a limited number of pins, and we stabilize noisy values using moving average processing. In addition, an LCD monitor allows the user to check various values in real time without connecting to a PC.
In preparation for the world championships, we reviewed our robot’s design. The shape of the robot, which used to differ between the attacker and the goalkeeper, is now unified. By adopting two identical robots that combine the advantages of both roles, it is now possible to switch roles immediately during a match. Furthermore, all sensors and circuit boards are also standardized, resulting in improved parts management and even higher compatibility. You can follow our activities on X (formerly Twitter). We also publish all our data on GitHub.
11.1V
11.1V
Battery
:Kypon
1300mAh/ 3s /11.1V
11.1V
Multiplexer
＞ピンを増やす
ことが可能
Digital
Analog
Main Controller
:Teensy 4.0
・Used to control motors
and sensor processing
・High processing speed
Sub
Controller
:Seeeduino XIAO
・ Smaller and with more pins.
Multiplexer
・Possible to
increase the
number of pins
Ball sensors
:TSSP58038× 16
Solenoid
:CB1037 x 1
Motor
:DIGILENTIG22 1/19
・12V drive system,
cheap and fast.
・Delicate movements
possible.
X 4
Motor Driver
DAISEN DSR-1202
IC:VNH2SP30 x 4
・0.3V ~ 16.0V
・15~30A
Gyro Sensor
:AE-BNO055-BO
・Create a board that can
be replaced with L3GD20H
Kicker System
:XL6009
11.1V
48V
5.0V
UART
UART
Digital
I2C
UART
Voltage
Conversion Circuit
Using IC :
OKL-T/6-W12N-C
11.1V to 5.0V
Analog
Sub
Controller
:Seeeduino XIAO
＞小さくてピンの数も多い
Line Sensors
:NJI7502
Debug System
O-LED Display
：SSD1306
Tactile Switch x 3
Robot’s Structure
Vision System
・Goal angle and court center detection
Omnidirectional Mirror
OpenMV H7
UART
UART
The motors we used on the robot last season
were 6-volt motors, which limited its speed and performance.
So we decided to look for faster and more efficient motors.
While keeping costs as low as possible, we chose 12-volt motors.
As a result, we came up with the following motor options.
・ DC geared motor 12V 1:19（DIGILENT IG22 1/19）
（ about 19 dollars ）June 2024
This motor had the performance we were looking for and
we thought it was a good choice. However, while this motor
increased the speed, it caused more out of bounds.
So, even if the robot is fast, it's meaningless if it goes out of bounds.
In the past, the motor speed was reduced to prevent out of bounds,
but there was a problem with the motor continuing to accelerate as it was. To solve this problem, we decided to use the BNO055 to measure the robot‘s speed. This allows us to reduce its speed near the boundary lines to prevent out-of-bounds, while allowing it to reach maximum speed at the center of the court.
Experimental environment
For the Verification 1 and Verification 2 experiments, we ran the robot from one end of the court to the other and used a recording timer to measure the distance traveled every 0.1 second. Based on these measurements, we calculated the average speed for each 0.1-second interval and created a graph showing how the speed changed over time. （See Photos 1 and 2）
「 Speed control 」
determine the set speed. If the measured speed is
below the set speed, increase the motor power.
Conversely, if the speed exceeds the set speed,
decrease the motor power.
This method is called "speed control."（See Figure 1）
We conducted the following verification to evaluate whether
this method is effective in preventing out of bounds.
Verification 1:
Exploring the difference between speed control and no control. To verify that the speed control was functioning correctly, we conducted experiments both with and without speed control.
Next, we compared the relationship between velocity (v: cm/s) and time (t: seconds) using graphs.
Result：
The graph shows that the speed is constant at 80 cm/s with speed control compared to without.
Verification 2:
Comparison of Deceleration Characteristics With and Without Speed Control.
The graph compares the relationship between velocity (v: cm/s) and time (t: seconds) in two cases.
In the first case, the robot was accelerated to a set speed using speed control, and then decelerated by reducing that set speed. In the second case, the robot was operated without speed control at a fixed PWM value for a certain time, and then decelerated by reducing the PWM value.
Result：
The graph shows a case where the final speeds after deceleration are approximately equal with and without speed control. In this example, the time required to decelerate to the set speed is shorter with speed control than without it, even though the initial speed was higher with speed control. This indicates that speed control is more effective for deceleration. (See Graph 2)
Verification 3:
Find the maximum value of the speed that is not out of bounds
The goal was to find the maximum speed at which the robot could stop without going out of bounds and hitting a wall when stepping on the line. We created a program to brake when stepping on the line, varied the set speed, and recorded the maximum speed that did not go out of bounds.
The results show that a set speed of 600 is the maximum optimal speed at which the robot can stop without going out of bounds. Therefore, this speed was set as the maximum speed when near the line. In other areas , we decided to use speed control with no upper speed limit.
(See Table 1)
For position estimation, a camera is used to estimate the position of the robot based on the direction of the center of the court.
Conclusion：
From Verification 1, it was observed that without speed control, the robot’s speed continues to increase, whereas with speed control, the speed eventually stabilizes.
From Verification 2, it was shown that the motor with speed control decelerates more quickly than the one without it.
From Verification 3, the maximum speed at which the robot can stop without going out of bounds was identified. Previously, this speed had been manually adjusted through trial and error.
Comparison of Speeds Without Going Out of Bounds
▷Photo１ The experiment scene
▷Photo２ The experiment scene
Speed control that leads to improved line control
▷Fig2
Data / Results / Discussion
Verification1
Verification2
Verification3
Speed instability
Slow deceleration
Quick deceleration
Speed stability
Unclear maximum speed
Clear maximum speed
As a result of this test, the following is now possible
Set speed
Fast
Slow
▷Fig1 Mechanism of speed control
▷Gragh2
▷Gragh1
Effect of Speed Control on Deceleration
Effect of Speed Control on Velocity Stability
▷Gragh3
Effect of a Moving Average Filter
私たちのチームは、ロボカップサッカー・ライトウェイト部門に昨シーズンから参加しており、今年で結成2年目となります。メンバーは4人で、そのうち3人は高校から、1人は中学からロボット競技に取り組んできました。それでも、私たちは「世界大会優勝」という大きな目標を掲げ、日々ロボット製作や技術向上に励んできました。
限られた時間の中で、チーム全員が着実に成長できるよう、明確な活動方針を定めて取り組んできました。
今回は、私たちがどのような方針のもとで活動を進めてきたのか、その内容をご紹介したいと思います。
チームメンバーの一人一人がロボットを製作し、ロボットの構造や仕組みについて理解を深めました。
１年目（前半）
ロボット製作を通して自分自身の得意分野や不得意分野を見つけ出し、それをに応じてチーム内の担当を決めました。
１年目（後半）
ジャパンオープンの反省を踏まえ、
実装したい機構を話し合い、
必要な技術を検討した上で
計画を立て、手順を明確にしながら技術力を高めていきました。
2年目（前半）
2年目（後半）
世界大会に向けて
世界大会優勝
過去の試合経験を元に
さらに実装したい機構や戦略について話し合い、世界大会に向けてどんな準備が必要かをチームで話し合いました。
目標
ジャパンオープンでの
経験を踏まえて、
世界大会に環境にも
適応するために
何をすればいいのか話し合いました。
Ⅾaily accumulation and planning are important
また、私たちは技術力を高めるために、これまで莫大な時間を費やし、並々ならぬ努力を積み重ねてきました。
土日には朝10時から夕方5時まで、平日もほぼ毎日、学校終わりの16時から19時まで活動を続けてきました。
右のグラフは、私たちがロボット製作に費やした累積の活動時間を月ごとに示したものです。縦軸はロボットに関わった時間（分）、横軸は月日の経過を表しています。このグラフは、限られた時間の中で世界を目指し、私たちが必死に積み上げてきた努力の軌跡です。
私たちの総活動時間は、約180,000分（約3,140時間）にのぼります。 この膨大な時間は、「毎日の小さな努力の積み重ねが、やがて大きな成果に結びつく」と信じ、全力で取り組んできた証です。
私たちは、ロボットを作るだけでなく、“努力する力”そのものをチームで磨いてきました。失敗も成功も、自分たちの手で経験してきたからこそ、
「努力を続けることが、成長と成果を生む」ということ、そしてそれが強いロボット製作につながるということを、私たちは心から実感しています。
1
2
３
7
6
8
9
５
４
Robot 1,2
Actual screen
stand-alone camera
Omnidirectional camera
This composition allows the robot to constantly monitor its surroundings with a single camera, and to acquire and process information such as the position of the goal and the direction of the center of the court in real time. With fewer sensors than before, enables a wider and more efficient recognition of the environment, contributing greatly to posture control and line control that always faces in the direction of the goal.
Before introduction
Of multiplexer
After introduction
Of multiplexer
Wired to curve
Old capture zone
New capture zone
This season's frame
Last season's frame
Chart: 
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95 | 1.05 | 1.1499999999999999 | 1.25 | 1.35 | 1.45 | 1.55 | 1.65 | 1.75 | 1.85 | 1.95 | 2.0499999999999998 | 2.15 | 2.25 | 2.35 | 2.4500000000000002
with speed control | 18 | 36 | 48 | 62 | 69 | 74 | 78 | 80 | 83 | 82 | 81 | 82 | 79 | 79 | 81 | 80 | 78 | 80 | 79 | 78 | 78 | 80 | 79 | 82 | 79
without speed control | 23 | 47 | 61 | 68 | 72 | 75.5 | 77.5 | 78 | 80.5 | 82 | 83 | 85 | 83 | 86 | 87 | 88 | 90 | 91 | 89 | 88 | 88 | 87 | 88 | 90
(v: cm/s)
(t: seconds)
Chart: 
| 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95 | 1.05 | 1.1499999999999999 | 1.25 | 1.35 | 1.45 | 1.55 | 1.65 | 1.75 | 1.85 | 1.95 | 2.0499999999999998 | 2.15 | 2.25 | 2.35 | 2.4500000000000002
with speed control | 43 | 60 | 73.1 | 87 | 93 | 102 | 106 | 111 | 117 | 119 | 120 | 121 | 120 | 105 | 89 | 70 | 61.5 | 50.1 | 36 | 30 | 27 | 29 | 26 | 26 | 27
without speed control | 51 | 57.1 | 59 | 67.5 | 77.5 | 85 | 91.5 | 95 | 99.5 | 102 | 105 | 107 | 106.5 | 92 | 79 | 70 | 62 | 55.1 | 45 | 34 | 32 | 33 | 30 | 28 | 29.5
(v: cm/s)
(t: seconds)
Chart: 
Analog value
Number of readings
Evaluation of Optimal LED Color for Line Sensors
Our line sensors have been using white LEDs until now, We decided to experiment with the question of whether white LEDs are really suitable. We are using full-color LEDs in the experiment that can change the color and brightness of the light. We made a graph and a table of the data when the robot passed a white line using red, green, and blue light compared to the white light we had used before.
Looking at Figure 1, it’s easy to assume that white light is advantageous because the response values are high. However, it’s also evident that the values when there is no response are higher compared to those of other colors.
For line sensors, a greater difference between the minimum and maximum values is more advantageous.
Comparing the differences in Figure 2, red and blue show a larger range than the other two colors. However, blue is a prohibited color and cannot be used.
Therefore, it can be concluded that the most suitable light source for the sensor is red.
Response Values by Color
Max-Min Difference for Each Color
▷Gragh4
▷Gragh5
Chart: 
Chart: 
| blue | green | red | white
 | 270 | 250 | 277 | 227
今田 耕司様